## Slide 1: Some Observations on Mash pH Prediction/Control
J. deLange
MBAA District Mid Atlantic Fall Meeting,
Frederick, MD
8-9 November 2013

## Slide 2: Background
Brewers who study water do so with 2 goals in mind:
  Getting mash pH into proper range
  Adjusting ‘stylistic ions’ for desired flavor
    Hops perception (sulfate)
    Body/mouthfeel, sweetness, roundness (chloride)
This talk presents a slightly different perspective on the acid/base chemistry of mash pH prediction
Based on work for John Palmer’s water book.
  “Water: A Comprehensive Guide for Brewers”

## Slide 3: MOTIVATION
pH controls electrical charge on molecules/ions
Charge controls shape of enzymes (proteins)
Enzyme shape controls enzyme performance in mash, fermenter….
Get mash pH right (essential) and pH more or less falls into place for the rest of the process
If you are making good beer you are controlling pH – explicitly or implicitly
Goal Today: Insight/tools to help you do this
Model is simple acid base chemistry with a twist.
  Getting malt data for that model is the hard part.

## Slide 4: Agenda
Slightly different perspective on pH and the calculations of acid/base chemistry
Emphasis on Proton Deficit: the amount of acid required to move pH to a target value
New (I think) way of modeling malt proton deficit (acidity or alkalinity) as a simple Taylor series expansion about malt DI pH
  A couple (2 -3) coefficients suffice

## Slide 5: What is pH?
‘Invented’ by S. P. L. Sørenson at Carlsberg Lab.
IUPAC Definition: pH = -log10(activity of H+) in a solution (aqueous in brewing).
  H+ ion is a proton
  Activity is approximately the concentration in moles/L
Formal definition of little use to us here
We are concerned with relationship between pH and electrical charge on molecules.

## Slide 6: Moles, Equivalents
A mole (mol) is 6.02 x 1023 objects
Molecules: A ‘gram molecular weight’ of the substance contains 1 mol
  Example: Carbonic acid: GMW = 62 g/mol
  62 g carbonic acid: 6.02 x 1023 H2CO3 molecules
  Calcium metal: GMW = 40 grams/mol
Electronic charges: A ‘gram equivalent weight’ contains 1 mol of electronic charge (1 Eq)
  GEW of Ca++: 20 g/Eq ~ 20 mg/mEq
  20 mg Ca++ has 1 mmol (6.02 x 1020) electronic charges = 1 mEq (milliequivalent)
  20 mg Ca++ contain 1/2 mmol calcium ions

## Slide 7: Carbo, CT
A term for the sum of the molar concentrations of carbonic acid molecules, bicarbonate ions and carbonate ions
The sum of the moles of carbon in those three species
Used to distinguish these carbons, in water, from carbon in malt compounds….
Carbo is a term that we’ll use fairly frequently

## Slide 8: How pH Controls Electric Charge Carbonic Acid 1st Proton
Constant for 1st proton only
Law of Mass Action
If total carbo is 1 mmol/L
Charge on carbo is (0.5)(-1) + (0.5)(0) = -0.5 mEq/L
Reaction goes either way
Henderson - Hasselbalch

## Slide 9: How pH Controls Charge Carbonic Acid 2nd Proton
Constant for 2nd proton only
Law of Mass Action
Henderson - Hasselbalch
If total carbo is 1 mmol/L
Charge on carbo is (0.5)(-2) + (0.5)(-1) = -1.5 mEq/L

## Slide 10: Lowering pH Increases Charge
pH 6.38: Q = -0.5
pH 10.38: Q = -1.5
Making the charge less negative is increasing it.
Charge on
1 mmol Carbo
Curve shows charge on 1 mmol of Carbo

## Slide 11: How We Estimate/Control Mash pH
By keeping track of the protons required to effect charge changes that we either
  Measure directly (malt titration)…
  …or calculate from measured parameters (water alkalinity, phytin reaction, acid base additions)
To help us do this we define ‘Proton Deficit’
  Proton Deficit: The number of protons that must be supplied to effect a pH (charge) change
  If the number to be supplied is negative this means protons must be absorbed.

## Slide 12: Proton Deficit (PD)
With respect to a particular pH
  If PD > 0 it is the quantity (mEq) of protons (H+ ions) which must be added to a unit amount of a mash component lower its pH to the pH of interest
    You know it as Alkalinity from your water reports
  If PD < 0 it is the -1 times the quantity (mEq) of protons which must be absorbed from a unit amount of a mash component to raise its pH to the pH of interest
    You may know it as Acidity from your water reports
    A deficit of –10 mEq is a surfeit of +10 mEq

## Slide 13: Mash pH
Is the pH at which total proton deficit = 0.
  Each relevant mash component has a positive or negative proton deficit
  They sum to 0 at the mash pH.
Relevant mash components:
  Water bicarbonate and carbonate ions ( > 0; alkalinity)
  Base malt ( > 0; alkalinity)
  Specialty malts ( > 0; alkalinity or < 0; acidity)
  Any acids (< 0) or bases (> 0) added by the brewer
  H2PO4- (malt) + Ca++ (water) (< 0 – proton source)

## Slide 14: Example of Alkalinity (PD > 0)
If 2 mmol (168 mg) sodium bicarbonate is added to 1 L distilled (DI) water the pH will be ~ 8.32
To get to pH 5.4 must add 1.81 mEq acid (protons, H+ ions) per L e.g. 1.81 mL N acid.
  There is a proton deficit of +1.81 mEq/L wrt pH 5.4.
  The alkalinity of this water is 1.81 mEq/L wrt pH 5.4
To get pH 4.3 must add 2.03 mEq/L protons
  This is M (methyl orange) or T (total) alkalinity of a water sample.
  As CaCO3: 2.03 mEq/L ~ 50*2.03 = 100.15 ppm as CaCO3

## Slide 15: Alkalinity (PD > 0), 2nd Example
If I mash a particular Pilsner malt in DI water the pH will go to 5.64 (20°C)
If I want pH 5.4 I must add 9.3 mEq protons/kg
  Proton deficit wrt pH 5.4: 9.3 mEq/kg
  Alkalinity wrt pH 5.4: 9.3 mEq/kg
If I want pH 5.3 I must add 14.3 mEq/kg acid
  Proton deficit/Alkalinity wrt pH 5.3: 14.3 mEq/kg
Alkalinity always with respect to some pH
  Water P-alk: pH 8.3 Water M(T)-alk: pH 4.3

## Slide 16: Acidity (PD < 0) Example
If I mash 1 kg of a particular 600L chocolate malt in DI water the pH will be 4.70
To get pH 5.3 I must absorb 46.5 mEq protons
  There is a proton surfeit of 46.5 mEq/kg. This is called the acidity of the malt with respect to (wrt) pH 5.3
  Proton deficit wrt pH 5.3: – 46.5 mEq/kg.
Acidity is always wrt some pH
  Example: Water P-acidity is wrt pH 8.3

## Slide 17: Mash pH
If chocolate malt and Pilsner malt are mixed in water containing bicarbonate:
  Chocolate malt will give up protons (PD < 0)
  Base malt and bicarbonate will absorb protons (PD > 0)
  Mash pH: pH at which sum of base malt and bicarbonate alkalinity equal chocolate malt acidity - PD = 0.
Finding mash pH: calculate sum of proton deficits at various pH values until PD = 0.
  This is done by a directed iterative process such as the Excel Solver.

## Slide 18: Grist Component Proton Deficits
Phosphate/Calcium
Base Malt pHBM
Specialty Malts pHSM
Weak Acids pH0
Strong Acid/Base
Water
pHW
+
Total Proton
Deficit (TPD) = 0
Control: Set trial pH to desired target pH. Add acid/base, change
specialty malt amounts, add calcium until TPD = 0
Estimation: Find trial pH at which TPD = 0
Trial pH
> 0
> 0
</> 0
< 0
< 0
< 0

## Slide 19: Calculating Proton Deficits
Strong acid (H2SO4, HCl, HLac...): deficit is minus normality e.g. 1 N HCl deficit = -1 mEq/ml
Strong Base (NaOH, Ca(OH)2): deficit is normality e.g. 1 N NaOH deficit = +1 mEq/mL
Water: Deficit computed from pH and Alkalinity
Water Calcium/Malt Phosphate reaction: deficit is -1 times the number of protons released. Estimated
Malt: deficit calculated from ‘titration’ curve for each malt.

## Slide 20
Alkalinity
Acidity
Fractions: Carbonic Bicarbonate Carbonate
Charge:
pHs
pHz
Alkalinity, pHs to pHz
0.84 mEq/mmol
Henderson-Hasselbalch Equation
Water Step 1: Charge, Q, on 1 mmol Carbo

## Slide 21: Water: Step 2 - How Much Carbo (CT)?
Example
pH: 7.6
Alk: 100
CT: 2.1 mmol/L

## Slide 22: Measure Alkalinity Yourself
To 0.1 L of water add 0.1 N acid in small increments.
Each mL of 0.1 N acid ~ 1 mEq/L
Record pH & total mL after each addition
M alkalinity is number of mL used to reach pH 4.3 (ISO pH: 4.5)
PD with respect to desired pHZ is number mL acid used to reach pHZ.

## Slide 23: Example Alkalinity Titration
Read PD/L directly from curve at pHZ of interest
Read M-alkalinity at pH 4.3

## Slide 24: Phosphate Similar to Carbo

## Slide 25: Malt
Malt contains phosphate and many other acids
Impossible to enumerate
Instead we measure proton deficit directly as we did for water two slides ago.
Acid system very complex but fits simple model:
  Taylor series expansion:
- a1, a2, a3 are coefficients descriptive of the malt
- pHDI is the distilled water mash pH for the malt
mEq/Kg

## Slide 26: Specs for 3 Malts 25 minutes, 20°C
 | DI Mash pH | a1 1st Coeff | a2 2nd Coeff | a3 3rd Coeff
Weyermann Pils | 5.65 | -40.69 | 14.82 | 10.01
Briess Caramel 80L | 4.76 | -89.68 | 31.84 | -10.06
Crisp Chocolate 500L | 4.71 | -76.43 | -0.404 | -3.615
Note: a1 is a measure of buffering capacity (the resistance of
the malt to change in pH) at the DI mash pH

## Slide 27: Malt Titration Difficult Compared to Liquor
Weigh out ground malt sample
Add to metal beaker with warmed mash water + acid or base
Place in water bath
Record pH at 20, 25, 30… min
  pH drifts over time
Discard and repeat for another sample with a different amount of acid or base

## Slide 28
Example Malt Measurements
23 measurements – 3/4 hour each

## Slide 29
Malt Proton Deficit
pHZ
Proton Deficit: 0.9 mEq/kg
pHDI
- Curve shifts with time
- Curve shifts with temperature 0.0055 pH/°C. Compute at other temperatures
by shifting pHDI by this amount. Coefficients stay the same!

## Slide 30: Proton Deficits of Base (Pils) and Two Specialty Malts
1 mEq ~ 1 mL
1 N acid or base

## Slide 31: Calcium, Magnesium, Phosphate
10Ca++ + 6H2PO4- + 2H2O  Ca10(PO4)6(OH)2 + 14H+
  Apatite, Ca10(PO4)6(OH)2, is least soluble of other calcium/magnesium salts which may also precipitate
Kohlbach’s residual alkalinity (RA): RA = alkalinity – [Ca++]/3.5 - [Mg++]/7 (mEq/L)
Implications:
  Each mEq/L Ca++ yields 1/3.5 = 0.286 mEq/L protons
  Each mEq/L Mg++ yields 1/7 = 0.143 mEq/L protons
  Ca++ and Mg++ can be thought of as acids
  But they are not, of course, actually acids.

## Slide 32: Can We Improve on Kohlbach?
With malt titration data we should be able to add a bolus of calcium to a sample and note the pH shift
From the slope of the malt curve (the buffering capacity) we can calculate the proton surfeit associated with that calcium bolus
We have not as yet investigated this concept

## Slide 33: Method
Build a spreadsheet which calculates deficits for malt, water alkalinity, phosphate/calcium protons, added acids/bases as a function of a trial pH
Include a cell in which they are summed
Try different pH values until the value that zeroes the sum is found
  Let the Solver (Excel) do this automatically
0 sum PD pH is the estimated mash pH
To set pH to desired value adjust grist components until sum PD = 0 at desired pH

## Slide 34: Directed Search (Root Bisection)
L
•
•
H
•
•
H
S
L
•
•
H
S
L
Guess lowest possible (L=4) and highest (H=7) pH’s
PD Sign change going from L to H verifies solution L < S < H
Move H to halfway between L and H (bisect)
Sign change between L and H? Yes: continue from 3
Else: Restore H to original position and move L to halfway
5. Continue from 3
pH
S

## Slide 35: Three Mash pH predictions
30 kg Pils + 3 kg 600L Chocolate Malt + 3 kg 80L Caramel Malt in 100L water
Differences: models and data fed into models
  Not claiming model being presented here is best
Ca+2 ppm as CaCO3 | Alkalinity ppm as CaCO3 | EZ | Brewers Friend | This Presentation
0 | 0 | 5.54 | 5.37 | 5.39
0 | 100 | 5.64 | 5.59 | 5.49
100 | 100 | 5.61 | 5.54 | 5.46
 | Grist Buffering  | -37.2 mEq/kg•pH | -37 mEq/kg•pH | -52.6 mEq/kg•pH

## Slide 36: Summary
pH prediction/control is important
Proton deficit is simple tool for prediction/control.
Models for malt, bicarbonate, water, calcium/phosphate, acid base proton deficits are simple
But it takes a lot of work to get good data to put into malt model
More work needed
  Can malt data be obtained more easily?

## Slide 37: Questions?
aj@wetnewf.org
www.wetnewf.org
703 624 8222